## Slide 1: An OpenFlow based virtual network environment for Pragma Cloud virtual clusters
Kohei Ichikawa, Taiki Tada, Susumu Date, Shinji Shimojo (Osaka U.),
Yoshio Tanaka, Akihiko Ota, Tomohiro Kudoh (AIST), Cindy Zheng, Philip Papadopoulos (UCSD)

## Slide 2: Background
VM deployment project
  Since the PRAGMA 20, we have been starting VM deployment project on the PRAGMA testbed.
Despite the development of Grid and Cloud technologies, it is still hard to deploy a single virtual computation environment like a local cluster among multiple organizations because of heterogeneities of resources and networks.
VM repos.
Gfarm
VM
VM
VM
VM
VM
Condor Job pool
Download VM image from Gfarm repos.
Deploy the VM
Add the VM into a Condor job pool
Network connectivity across heterogeneous Firewalls/NATs is still big problem.
  Some sites could not connect to Gfarm because of firewall policy.
  Private nodes behind NATs could join this project.
Prof. Shimojo suggested using OpenFlow to virtualize the network.

## Slide 3: OpenFlow
  A centralized programmable remote controller dictates the forwarding behavior to multiple OpenFlow switches. This architecture separating forwarding plane from control plane allows flexible management to network operator.
  Utilized software tools for this demo:
    Trema (http://trema.github.com/trema/)
  A framework for developing OpenFlow controllers
    Open vSwitch (http://openvswitch.org/)
  A software based implementation of OpenFlow switch
OpenFlow Controller
OpenFlow Protocol
Flow control
programming
Open vSwitch
OpenFlow Switch
Network Operator
forwarding plane
control plane

## Slide 4: Overview of the demo environment
Provides an isolated virtual network for each VM project
Open vSwitch
Open vSwitch
Open vSwitch
Open vSwitch
Open vSwitch
Open vSwitch
Open vSwitch
Open vSwitch
Open vSwitch
Openflow Controller Trema (Sliceable routing switch)
Osaka Univ.
AIST
UCSD
Openflow network
GRE
GRE
GRE
GRE
GRE
GRE
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
Virtual network slice A
Virtual network slice B
As for the detailed technique, please see the Taiki’s poster session tomorrow

## Slide 5: Comparison between the past and the present approach
Condor Master
The past
The present
Condor master Admin
VM
VM
VM
VM
VM
Site A admin
Site B admin
Site C admin
Assign a new global IP for each VM launching
Configure firewall policy to pass the communication for Gfarm, condor and so on
Register the new launched VM’s IP to the condor pool
Condor Master
Condor master Admin
VM
VM
VM
VM
VM
Site A admin
Site B admin
Site C admin
Dedicated isolated virtual L2 network
Request IP via DHCP
Register the IP to the condor pool automatically

## Slide 6
Demo

## Slide 7: Basic performance of virtual network
Network latency (almost same as physical net)
  Osaka-AIST: 15.3ms
  AIST-UCSD: 118ms
  Osaka-UCSD: 115ms
Network throughput (get some overheads)
  Osaka-AIST: 589.98 Mbps
  AIST-UCSD: 32.99Mbps
  Osaka-UCSD: 42.16Mbps

## Slide 8: For next stage
Management of Multiple VM clusters
  manages virtual network slices on user’s demands
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
Virtual network slice A
Virtual network slice B
Physical Network
controls forwarding rules
OpenFlow Controller
defines virtual slices
UI
Request&manage new slices
Missing part